## Slide 1
Target
  Use the same push button to shutdown the system and to restart it without unpligging power supply
Principals
  If system is up, send 3.3V on a GPIO PIN to detect when button is pushed to shutdown the system (init 0)
  If system is dow, send 3.3V on RESET PIN to restart the board
  To switch between RST PIN and GPIO PIN, we gonna use a 2 position relay
    0 : circuit to RST
    1 : circuit to GPIO PIN (lets say GPIO4 on header PIN16)
  We’re going to control the relay with an other GPIO (lets GPIO5 on header PIN18)

## Slide 2
Setup the board
  By default the Rasp board have a RST pin but it's not sold out. Up to you to solder a pin on the board. It's between the GPIO connectors and the display connector
  It’s the 2 small holes with pills to solder :
    One is +3.3V the one is RESET
+3.3V
RESET

## Slide 3
Setup the board
  After jour job, it should look like this

## Slide 4
0
1
VCC 3.3V
Reset PIN
GND
GPIO5
(PIN 18)
GPIO4
(PIN 16)
Schematic

## Slide 5
Main code
  First of all, install wiringPI http://wiringpi.com/download-and-install/
  Script to run at startup (daemon)
    #!/bin/bash
    (
    RELAY_GPIO=5
    BUTTON_GPIO=4
    trap stopRelay 1 2 3 6 9 14 15
    function stopRelay(){
    gpio write $RELAY_GPIO 0
    }
    gpio mode $RELAY_GPIO out
    gpio mode $BUTTON_PIN in
    gpio write $RELAY_GPIO 0
    while [ 1 ] ; do
    BUTT=`/usr/local/bin/gpio read $ BUTTON_PIN `
    while [ $BUTT -eq 1 ] ; do
    sleep 0.2
    BUTT=`/usr/local/bin/gpio read $ BUTTON_PIN `
    done
    init 0
    done
    ) &
  Create a service (init.d script) from /etc/init.d/skeleton